## Slide 1: Lab Work CPT-based Cs microcell Atomic Clock
Marion Delehaye, Clément Lacroûte, Cyrus Rocher, Gilles Martin, Philippe Abbé, Rodolphe Boudot

## Slide 2: Reminder: Linear Spectroscopy (cf. Mileti, Lacroûte)
Optical Absorption Medium
Very easy! Put a gas vapor in a glass cell!
Laser
Vapor cell
F=1
F=2
6.8 GHz
500 MHz
The lines are broadened by the Doppler effect

## Slide 3: Reminder: CPT in cell clocks (cf Mileti, Affolderbach)
Coherent Population Trapping (CPT)
2 coherent light fields,
Simultaneous preparation and interrogation
Laser source
Rb
cell
2 light fields: f1 – f2 = fHFS = fclock
u-wave source
Servo
loop
Det.
P
S
fuwave
transmission
≤ 1 %
Employs coherent laser effects  potential for new & improved clocks (first proposal: Cyr et al., IEEE TIM, 1993)
No microwave cavity needed  more radical clock miniaturization

## Slide 4
Lab work CPT clock
You will be able to control:
the VCSEL current and temperature
the magnetic field
the local oscillator frequency
the RF modulation power
You will be able to view:
the photodiode signal
laser and local oscillator error signals
the clock signal

## Slide 5
Lab work CPT clock – hardware

## Slide 6
Lab work CPT clock – software
The whole experiment is controlled by an Arduino controller, interfaced using a C software and a Python interface.
The GUI lets you input the commands as digital words within the command line.
Some parameters (laser diode current, magnetic field current) can also be input in their proper unit in the dedicated boxes.
You can view the commands and digital words actually sent to the micro-controller in the command window

## Slide 7
1 – Characterize the laser diode
2 – Linear spectroscopy
3 – CPT signal
4 – Lock the LO using the CPT signal
5 – Characterize the clock frequency stability
Lab work CPT clock – what you will do

## Slide 8
You may now start the lab work… by reading the printed labwork subject!

## Slide 9: CPT linewidth – influence of collisions
Buffer-gas: avoids ground-state relaxation by collisions with the cell walls.
Diffusion:
Collisions:
Spin-exchange coll.
Total:
Compromise on p, pCs => optimal T for a given cell (ie Cs + buffer gas mixture)
T, p, pCs are crucial parameters
gas
Cs
Collisions with the walls
Collisions with the buffer gas
Cs-Cs collisions

## Slide 10: Linear absorption – linewidth
The total width of absorption lines is determined by:
with where k is the Boltzmann constant, T is the temperature and m is the atom mass.
Natural width
Collisional broadening
(MHz/Torr)
Pressure
Doppler width

## Slide 11: Linear absorption – linewidth
The total width of absorption lines is determined by:
with where k is the Boltzmann constant, T is the temperature and m is the atom mass.
4,56 MHz
10-20 MHz/Torr
Pressure
Approx. 360 MHz @295 K

## Slide 12: Linear absorption – linewidth
The total width of absorption lines is determined by:
In practice, the line profile is a Voigt function (convolution of Gaussian and Lorentzian) from which one can extract both the temperature and the pressure broadening.
Lorentzian
Gaussian

## Slide 13: Linear absorption – linewidth
The total width of absorption lines can be roughly approximated by:
From a fit, one could extract T and β or p.
Here, we know T and β so we can deduce p.
A better approximation (0.02% error – source Wikipedia):

## Slide 14: Linear absorption – Beer-Lambert law
where L is the cell length and is the absorption coefficient given by
where is the Cs density inside the cell, and is the line wavelength.
Cs

## Slide 15: Linear absorption – Beer-Lambert law
where L is the cell length and is the absorption coefficient given by
where is the Cs density inside the cell, and is the line wavelength.
Here we know T and so we can deduce ie pCs.
Cs

## Slide 16
In summary:
Here we know T, L and β;
by measuring the optical linewidth and absorption we can deduce the buffer-gas pressure p and the Cs pressure pCs
rough estimate of expected CPT linewidth